# Digital Systems

Things you should learn:

- The concept of “analog”

- How information is represented in analog

- How physical processes and computation can be represented by analog devices

- Some problems with analog representation—stability, resolution, etc.

- The concept of “digital”

- The implications of continuous vs. discrete information states

- How digital representations of information eliminate problems associated with analog representations

- The tradeoffs between analog and digital systems—including economic considerations

- Why digital systems are almost always binary

- Binary representation of information and the base-2 numbering system

- Why octal (base-8) and hexadecimal (base-16) are useful numbering systems

- What George Boole developed and why it’s central to digital systems

- The three primitive logic gates that, together) can carry out every possible operation—computational or logical—in binary systems

- Truth tables, combinatorial logic, computation, and digital control

- Addition, subtraction, and multiplication in binary; two’s complement representation of negative numbers

- Why NAND gates (or NOR gates) rule the digital world

- John von Neumann’s concept of a digital computer

- Why this concept led to the digital revolution

- The evolution of digital technology and Moore’s Law

- Digital technology today—CPUs, memory chips, communication

Things you should be able to do:

- Identify and describe the operation of several everyday analog devices

- Create/invent an analog device to represent a process or calculation

- Convert quantities between binary, octal, and hexadecimal numbering systems

- Convert verbal logic statements into truth tables into logic circuits into physical circuits

- The inverse problem:  Evaluate a logic circuit and deduce its truth table

Things you should lie awake thinking about:

- Digital seems to be everywhere.  Are there instances where analog is better?

- Problems resulting in differential equations, integration, and differential—processes that are inherently continuous, must be “discretized” to be handled by digital systems.

- If Moore’s Law continues to hold for the foreseeable future, how long will it be before computers have the power/capacity of the human brain?